## Slide 2: Gust Load Alleviation Using Nonlinear Reduced Models For Control Law Design
N.D.Tantaroudas
K.J. Badcock, A. Da Ronch
University of Liverpool, UK
Bristol , 13 December 2012
FlexFlight: Nonlinear Flexibility Effects on Flight Dynamics
Control of Next Generation Aircraft

## Slide 3: Overview
Very large or very flexible aircraft
- low frequency modes-large amplitudes
- coupled rigid body/structural dynamics
TestCase-UAV configuration
-Modal Analysis(Nastran)
-Model Identification of the Structural Model-Implementation
-Model Order Reduction
-Gust Responses/Linear Aerodynamics(Strip Theory)
-Control design Using Reduced Models for Worst Gust Case

## Slide 4: Model Reduction
eigenvalue problem of Jacobian A
FOM projection onto aeroelastic eigenmodes

## Slide 5: UAV Configuration
DSTL UAV[P. Hopgood]
Wing
-Span:16.98m
-Taper Ratio:0.44
-Root Chord:1.666m
-Tip Chord:0.733m
-Control Surface:16/100chord
Tail
-Dihedral:45deg
-Taper Ratio: 0.487
-Root Chord:1.393m
-Tip Chord:0.678m
-Control Surface:25/100 chord

## Slide 6: Model Identification
Beam Reference system –j-node:
Finite Element equation-dimensional form :
Modal Analysis(Nastran)
Match the frequency of the low frequency modes
Match modeshapes
Limitations
High frequency modeshapes difficult to be matched

## Slide 7: Model Identification
From 2D plate to 1D beam model

## Slide 8: Mode Identification
Part | F -Hz | F Tuned -Hz | Modeshape
Wing | 1.51 | 1.45 | First Bending Mode
Wing | 4.92 | 6.27 | Second Bending Mode
Wing | 5.11 | 6.49 | First In Plane Bending Mode
Wing | 10.06 | 13.20 | Third Bending Mode
Wing | 14.48 | 13.99 | First Torsional Mode
Wing | 11.17 | 24.01 | Fourth Bending Mode
Wing | 19.39 | 28.26 | Second In Plane Bending Mode
Tail | 31.76 | 31.42 | First Bending Mode
Tail | 93.81 | 93.61 | Torsional Mode

## Slide 9: Model Identification
f=1.45Hz

## Slide 10: Model Identification
f=6.27Hz

## Slide 11: Model Identification
f=13.20Hz

## Slide 12: Model Identification
f=24.01Hz

## Slide 13: Model Identification

## Slide 14: Model Order Reduction
-Wing Tip Vertical Deflection Time Response Without Aerodynamics
Harmonic Follower Force
-ROM/NROM –structural eigenvalues

## Slide 15: Aeroelastic Gust Responses
-Wing tip vertical displacement
Reduced Basis-Structural

## Slide 16: Aeroelastic Gust Responses
-Wing tip vertical displacement
Reduced Basis
-Structural +Aero

## Slide 17: Worst Case Gust
1 minus-Cosine Gust for
several gust lengths

## Slide 18: Worst Case Gust-Reduced Models

## Slide 19: Worst Case Gust-Reduced Models
FOM linear beam
ROM linear beam
FOM nonlinear beam
ROM nonlinear beam

## Slide 20: Control Design Using Reduced Models
Linear Controller
Tuning Parameters
:control input
weight
:noise weight
Linear Reduced
Order Model

## Slide 21: Control Design Using Reduced Models

## Slide 22: Control Design Using Non Linear Reduced Models

## Slide 23: Control Design Using Non Linear Reduced Models

## Slide 24: Control Design Using Non Linear Reduced Models

## Slide 25: Non Linear Restoring Forces-Stability
3dof of freedom aerofoil

## Slide 26: Non Linear Restoring Forces-Stability
hardening spring
softening spring->instability
3dof aerofoil
1 minus cosine Gust
Softening Spring
Linear Control Design in this case??

## Slide 27: Instability
Instability

## Slide 28: Conclusions-Future Work
Reduced Basis identified with Linear Aerodynamics
-Structural eigenvalues - not always perfect descriptions when gust included
-Structural+aero - for improved predictions
Linear Control techniques suitable for Non Linear Structures
-Structural Nonlinearity  stability of the system
Future Work
-Introduction of the rigid body and flight dynamics in Beam Framework
-Control of the DSTL UAV with gust
-Softening nonlinearity  need for Non Linear Control?